PCM  Connector C1 Blue

Pin # Wire Color Circuit # Function 1 N/A 2 N/A 3 WHT 1310 EVAP Canister Vent Solenoid Valve 4 BRN/WHT 633 Camshaft Position Sensor 5 N/A 6 N/A 7 YEL 400 VSS Signal return 8 N/A 9 PNK/BLK 1746 VSS Signal return 10 N/A 11 DK BLU 229 VATS fuel enable 12 LT BLU/BLK 844 Injector #4 Control 13 RED/WHT 2122 Ignition coil 2 control 14 DK GRN 49 AC clutch status 15 BLK/WHT 845 Injector 5 control 16 N/A 17 N/A 18 YEL/BLK 846 Injector 6 control 19 N/A 20 N/A 21 PPL 719 IAT Sensor low 22 DK BLU 1225 Transmission range switch signal B 23 LT GRN/BLK 1745 Injector 2 control 24 BLK/WHT 1704 Ground jumper to other PCM connector 25 PNK 1224 Transmission range switch signal A 26 N/A 27 RED/BLK 877 Injector 7control 28 N/A 29 N/A 30 GRY/BLK 1687 TCS spark retard 31 DK BLU/WHT 878 Injector 8 control 32 ORN/BLK 434 P/N switch (grounded in park and neutral) 33 BLK 1744 Injector 1 control 34 GRY or WHT 587/687 3-2 Shift solenoid control 35 LT GRN 1222 1-2 Shift solenoid control 36 DK BLU 1936 Fuel level signal to gauge cluster 37 BRN/WHT 437 MIL control ( - output to MIL light) 38 N/A 39 DK GRN/WHT 459 A/C request 40 WHTorYEL/BLK 375/1223 Skipshift light, or 2-3 shift solenoid control 41 BRN/WHT 1173 Low oil level light control 42 LT GRN 1652 Reverse lockout solenoid (MT only) 43 DK GRN 335 Low speed cooling fan relay control ( - output) 44 YEL 573 Crankshaft position sensor signal 45 DK GRN/WHT 428 EVAP purge solenoid 46 N/A 47 DK GRN/WHT 762 A/C request 48 YEL 492 MAF sensor signal 49 PPL 2121 Ignition coil 1 control 50 N/A 51 N/A 52 PPL/WHT 2128 Ignition coil 8 control 53 RED 2127 Ignition coil 7 control 54 LT BLU/WHT 2126 Ignition coil 6 control 55 DK GRN/WHT 817 VSS signal out 56 DK GRN 2125 Ignition coil 5 control 57 DK GRN/WHT 2124 Ignition coil 4 control 58 LT BLU 2123 Ignition coil 3 control 59 BRN/WHT 2130 Reference low even coils 60 BRN 2129 Reference low odd coils 61 RED 1226 Transmission range switch signal C 62 BLK 552 EGR ground 63 BLK 407 A/C pressure sensor ground 64 N/A 65 N/A 66 N/A 67 N/A 68 N/A 69 N/A 70 N/A 71 PPL 401 VSS low reference 72 BLK 451 Ground 73 N/A 74 N/A 75 GRY 720 Fuel tank sending unit ground 76 BLK 451 Ground 77 PPL 420 TCC stop switch, + 12V until brake pedal is depressed 78 N/A 79 N/A 80 N/A

PCM connector C2 Red

Pin # Wire color Circuit # Function 1 TAN 1671 Bank 2 sensor 2 low reference 2 TAN/WHT 1669 Bank 1 sensor 2 low reference 3 TAN 800 Serial data UART to ALDL pin 9 4 RED 631 Camshaft position sensor 12v supply 5 TAN 1667 Bank 2 sensor 1 low reference 6 TAN/WHT 1653 Bank 1 sensor 1 low reference 7 RED/BLK 380 A/C pressure sensor signal 8 TAN 472 IAT sensor signal 9 BRN 1456 EGR pintle position 10 PPL 80 Fuel level sensor 11 N/A 12 DK BLU 417 TPS signal 13 YEL/BLK 1227 Trans fluid temp sensor signal 14 ORN/BLK 1057` Trans fluid temp sensor ground 15 N/A 16 N/A 17 N/A 18 N/A 19 PNK 439 Ignition power to 15A fuse 20 ORN 420 Battery + to 10A fuse 21 BLK 452 Ground 22 YEL/BLK 1868 Crankshaft position sensor low reference 23 BLK 451 Ground 24 BLK/WHT 1704 Jumper to other PCM connector 25 BRN 718 ECT sensor ground 26 ORN/BLK 469 MAP sensor ground 27 N/A 28 DK BLU 473 High speed cooling fan relay control (- output) 29 N/A 30 BRN 436 Air pump relay control 31 PPL 421 Air solenoid relay control 32 TAN/BLK 422 TCC solenoid control 33 BRN 418 TCC (PWM) Solenoid Valve Control 34 GRY 435 EGR ground 35 WHT 121 Tach signal out 36 LT BLU/WHT 1229 Transmission Fluid Pressure Control Solenoid Control Low 37 DK GRN/WHT 465 Fuel pump relay control 38 LT BLU 697 EGR valve control 39 RED/BLK 1228 Transmission Fluid Pressure Control Solenoid Control High 40 N/A

Pin # Wire color Circuit # Function 41 PPL 1670 Bank 2 sensor 2 Hi 42 PPL/WHT 1668 Bank 1 sensor 2 Hi 43 GRY 596 TPS 5V reference 44 N/A 45 N/A 46 PPL 1666 Bank 2 sensor 1 Hi 47 PPL/WHT 1665 Bank 1 sensor 1 Hi 48 LT GRN 432 MAP sensor signal 49 YEL 410 ECT sensor signal 50 N/A 51 N/A 52 DK GRN 890 Fuel tank pressure sensor signal 53 N/A 54 LT GRN/BLK 444 IAC coil B low control 55 LT BLU/BLK 1748 IAC coil A low control 56 LT BLU/WHT 1747 IAC coil A high control 57 LT GRN/WHT 1749 IAC coil B high control 58 PPL 1807 Serial Data to pin 2 of ALDL 59 N/A 60 BLK 451 Ground 61 ORN 340 Battery + to same 10A fuse as B+ above 62 LT GRN 1867 12V to crankshaft position sensor 63 N/A 64 GRY 461 MAP 5V reference 65 GRY 705 EGR 5V reference 66 GRY 474 A/C pressure sensor 5v reference 67 GRY 598 Fuel tank level and pressure 5v reference 68 LT BLU 1876 Rear knock sensor signal 69 DK BLU 496 Front Knock sensor signal 70 PNK/BLK 632 Camshaft position sensor low reference 71 N/A 72 N/A 73 N/A 74 N/A 75 N/A 76 BRN 1174 Oil level sensor signal in 77 N/A 78 N/A 79 N/A 80 N/A